## Slide 1: kathara lab
load balancer – web switch – random
Version | 1.1
Author(s) | Lorenzo Ariemma, Giuseppe Di Battista, Massimo Rimondini
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | A lab showing the operation of a web switch based on iptables – kathara version of a netkit lab

## Slide 2: Copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: lab topology
A
100.0.0.0/24
client1
eth0
10
client2
eth0
11
ws_random
WS
eth0
2
B
eth1
5
server1
WEB
eth0
1
10.0.0.0/24
server2
WEB
eth0
2
server farm
web switch
clients
server3
WEB
eth0
3

## Slide 4: lab description
servers
  offer a simple HTML default page
  each physical server hosts a different page, so that they can be easily distinguished
web switch
  web switch implements a policy for directing requests to the servers
    ws_random: sends each request to a random server
clients
  host a simple web browser (links)

## Slide 5: lab description – servers
each server has a different IP address in the subnet 10.0.0.0/24
no special configuration, just a simple HTML default page in /var/www/index.html

## Slide 6: lab description – web switch
each web switch has two interfaces
  one facing the internal network, with an IP address in the same subnet as the servers
  one facing the external network, exposing a single virtual IP address (VIP) to the clients
clients only see VIPs of the web switch: they do not know how many servers are in the farm

## Slide 7: lab description – web switch
web switch is implemented using the Linux firewall iptables
  random
iptables --table nat --append PREROUTING --destination 100.0.0.2 -p tcp --dport 80 --match statistic --mode random --probability 0.33 --jump DNAT --to-destination 10.0.0.1:80
iptables --table nat --append PREROUTING --destination 100.0.0.2 -p tcp --dport 80 --match statistic --mode random --probability 0.5 --jump DNAT --to-destination 10.0.0.2:80
iptables --table nat --append PREROUTING --destination 100.0.0.2 -p tcp --dport 80 --jump DNAT --to-destination 10.0.0.3:80
iptables --table nat --append PREROUTING --destination 100.0.0.2 -p tcp --dport 80 --match statistic --mode random --probability 0.33 --jump DNAT --to-destination 10.0.0.1:80
the rule applies with a certain probability

## Slide 8: experiments
to experiment load balancing, pick one of the clients, start links, and direct it to the VIP exposed by web switch:
to experiment random balancing
root@client1:~$ links http://100.0.0.2/

## Slide 9: experiments
once you have accessed one of the VIPs, you get a page stating which is the physical server that has served it
load balancing can be checked by reloading the page (ctrl+R), but...

## Slide 10: experiments
once you have accessed one of the VIPs, you get a page stating which is the physical server that has served it
load balancing can be checked by reloading the page (ctrl+R), but...
  ...by default all HTTP requests use the same connection (HTTP 1.1)!
  since iptables tracks TCP connections, all HTTP requests within the same connection are directed to the same physical server
  to really appreciate load balancing you need to close and re-open links