## Slide 1: kathara lab
static-routing
Version | 1.0
Author(s) | G. Di Battista, M. Patrignani, M. Pizzonia, F. Ricci, M. Rimondini
E-mail | contact@kathara.org
Web | http://www.kathara.org/
Description | an example of configuration of static routes – kathara version of netkit lab static-routing vers. 2.2

## Slide 2: copyright notice
All the pages/slides in this presentation, including but not limited to, images, photos, animations, videos, sounds, music, and text (hereby referred to as “material”) are protected by copyright.
This material, with the exception of some multimedia elements licensed by other organizations, is property of the authors and/or organizations appearing in the first slide.
This material, or its parts, can be reproduced and used for didactical purposes within universities and schools, provided that this happens for non-profit purposes.
Information contained in this material cannot be used within network design projects or other products of any kind.
Any other use is prohibited, unless explicitly authorized by the authors on the basis of an explicit agreement.
The authors assume no responsibility about this material and provide this material “as is”, with no implicit or explicit warranty about the correctness and completeness of its contents, which may be subject to changes.
This copyright notice must always be redistributed together with the material, or its portions.

## Slide 3: step 1 – network topology high level view
r1
100.0.0.8/30
195.11.14.0/24
200.1.1.0/24
r2
pc1
pc2

## Slide 4: step 1 – network topology configuration details
collision domain A
r1
r2
collision domain C
collision domain B
pc1
pc2
eth0
eth0
eth0
eth1
eth1
eth0
195.11.14.0/24
200.1.1.0/24
100.0.0.8/30
.5
.7
.1
.1
.9
.10

## Slide 5: step 2 – the lab
lab directory hierarchy
  lab.conf
  pc1/
  pc1.startup
  pc2/
  pc2.startup
  r1/
  r1.startup
  r2/
  r2.startup

## Slide 6: step 2 – the lab
ifconfig eth0 195.11.14.5 netmask 255.255.255.0 broadcast 195.11.14.255 up
pc1.startup
ifconfig eth0 200.1.1.7 netmask 255.255.255.0 broadcast 200.1.1.255 up
pc2.startup
r1[0]=A
r1[1]=B
r2[0]=C
r2[1]=B
pc1[0]=A
pc2[0]=C
lab.conf
#route add default gw 195.11.14.1 dev eth0
the routing table entries will be added manually
#route add default gw 200.1.1.1 dev eth0

## Slide 7: step 2 – the lab
ifconfig eth0 195.11.14.1 netmask 255.255.255.0 broadcast 195.11.14.255 up
ifconfig eth1 100.0.0.9 netmask 255.255.255.252 broadcast 100.0.0.11 up
r1.startup
ifconfig eth0 200.1.1.1 netmask 255.255.255.0 broadcast 200.1.1.255 up
ifconfig eth1 100.0.0.10 netmask 255.255.255.252 broadcast 100.0.0.11 up
r2.startup
#route add -net 195.11.14.0 netmask 255.255.255.0 gw 100.0.0.9 dev eth1
#route add -net 200.1.1.0 netmask 255.255.255.0 gw 100.0.0.10 dev eth1
the routing table entries will be added manually

## Slide 8: step 3 – testing connectivity
pc1:~# ping 195.11.14.1
PING 195.11.14.1 (195.11.14.1) 56(84) bytes of data.
64 bytes from 195.11.14.1: icmp_seq=1 ttl=64 time=3.17 ms
64 bytes from 195.11.14.1: icmp_seq=2 ttl=64 time=0.371 ms
64 bytes from 195.11.14.1: icmp_seq=3 ttl=64 time=0.308 ms
--- 195.11.14.1 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2019ms
rtt min/avg/max/mdev = 0.308/1.285/3.176/1.337 ms
pc1:~# █
pc1
r1
r2
pc1
eth0
eth0
eth0
eth1
eth1
eth0
195.11.14.5
100.0.0.9
195.11.14.1
200.1.1.7
200.1.1.1
100.0.0.10
pc2
interfaces on the same domain can reach each other

## Slide 9: step 3 – testing connectivity
r1
r2
pc1
eth0
eth0
eth0
eth1
eth1
eth0
195.11.14.5
100.0.0.9
195.11.14.1
200.1.1.7
200.1.1.1
100.0.0.10
pc2
pc1:~# ping 100.0.0.9
connect: Network is unreachable
pc1:~# █
pc1
interfaces on different domains cannot be reached
can you tell why?

## Slide 10: step 3 – inspecting routing tables
both routers and pcs don’t know how to reach networks that are not directly connected to them
directly connected networks are automatically inserted into the routing table when the corresponding interface is brought up
this is a common behavior of all ip devices (even real-world routers!)
pc1:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
195.11.14.0 * 255.255.255.0 U 0 0 0 eth0
pc1:~# █
pc1
r1:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.0.0.8 * 255.255.255.252 U 0 0 0 eth1
195.11.14.0 * 255.255.255.0 U 0 0 0 eth0
r1:~# █
r1

## Slide 11: step 4 – default routes on pcs
to fix the problem we could specify the default route on the pcs: “through this gateway (ip number) you can reach all the other networks”
pc1:~# route add default gw 195.11.14.1
pc1:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
195.11.14.0 * 255.255.255.0 U 0 0 0 eth0
default 195.11.14.1 0.0.0.0 UG 0 0 0 eth0
pc1:~# █
pc1
pc2:~# route add default gw 200.1.1.1
pc2:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
200.1.1.0 * 255.255.255.0 U 0 0 0 eth0
default 200.1.1.1 0.0.0.0 UG 0 0 0 eth0
pc2:~# █
pc2

## Slide 12: step 4 – default routes on pcs: test
pc1:~# ping 100.0.0.9
PING 100.0.0.9 (100.0.0.9) 56(84) bytes of data.
64 bytes from 100.0.0.9: icmp_seq=1 ttl=64 time=0.451 ms
64 bytes from 100.0.0.9: icmp_seq=2 ttl=64 time=0.299 ms
64 bytes from 100.0.0.9: icmp_seq=3 ttl=64 time=0.320 ms
--- 100.0.0.9 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2003ms
rtt min/avg/max/mdev = 0.299/0.356/0.451/0.070 ms
pc1:~# █
pc1
r1
r2
pc1
eth0
eth0
eth0
eth1
eth1
eth0
195.11.14.5
100.0.0.9
195.11.14.1
200.1.1.7
200.1.1.1
100.0.0.10
pc2
the “backbone interface” of r1 is reachable

## Slide 13: step 4 – default routes on pcs: test
pc1:~# ping 100.0.0.10
PING 100.0.0.10 (100.0.0.10) 56(84) bytes of data.
--- 100.0.0.10 ping statistics ---
7 packets transmitted, 0 received, 100% packet loss, time 6105ms
pc1:~# █
pc1
r1
r2
pc1
eth0
eth0
eth0
eth1
eth1
eth0
195.11.14.5
100.0.0.9
195.11.14.1
200.1.1.7
200.1.1.1
100.0.0.10
pc2
interfaces on r2 seem unreachable!
can you tell why?

## Slide 14: step 4 – let’s inspect the network
do echo request packets reach r2?
let’s check...
  while pinging from pc1 100.0.0.10 sniff on interface eth1 of r2
r2:~# tcpdump -i eth1
tcpdump: verbose output suppressed, use -v or -vv for full protocol decode
listening on eth1, link-type EN10MB (Ethernet), capture size 96 bytes
16:06:58.977851 arp who-has 100.0.0.10 tell 100.0.0.9
16:06:59.088906 arp reply 100.0.0.10 is-at fe:fd:64:00:00:0a
16:06:59.089990 IP 195.11.14.5 > 100.0.0.10: icmp 64: echo request seq 1
16:06:59.989368 IP 195.11.14.5 > 100.0.0.10: icmp 64: echo request seq 2
16:07:01.001888 IP 195.11.14.5 > 100.0.0.10: icmp 64: echo request seq 3
5 packets captured
5 packets received by filter
0 packets dropped by kernel
r2:~# █
r2
echo requests are arriving!
© Computer Networks Research Group Roma Tre

## Slide 15: step 4 – r2’s routing table
pc1’s address is 195.11.14.5
r2 does not know how to reach such an address.
echo requests arrive to r2 but r2 does not know where echo replies should be forwarded!
somebody should teach r2 how to reach pc1
we may insert a static route into the routing table of r2
r2:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.0.0.8 * 255.255.255.252 U 0 0 0 eth1
200.1.1.0 * 255.255.255.0 U 0 0 0 eth0
r2:~# █
r2

## Slide 16: step 5 – configuring a static route
r2:~# route add -net 195.11.14.0 netmask 255.255.255.0 gw 100.0.0.9 dev eth1
r2:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.0.0.8 * 255.255.255.252 U 0 0 0 eth1
200.1.1.0 * 255.255.255.0 U 0 0 0 eth0
195.11.14.0 100.0.0.9 255.255.255.0 UG 0 0 0 eth1
r2:~# █
r2
network 195.11.14.0...
...with netmask 255.255.255.0...
…is reachable via 100.0.0.9…
…on interface eth1

## Slide 17: step 5 – configuring a static route
a similar configuration should be deployed on r1
r1:~# route add -net 200.1.1.0 netmask 255.255.255.0 gw 100.0.0.10 dev eth1
r1:~# route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
100.0.0.8 * 255.255.255.252 U 0 0 0 eth1
200.1.1.0 100.0.0.10 255.255.255.0 UG 0 0 0 eth1
195.11.14.0 * 255.255.255.0 U 0 0 0 eth0
r1:~# █
r1

## Slide 18: step 5 – testing static routes
the pcs can reach each other
pc1:~# ping 200.1.1.7
PING 200.1.1.7 (200.1.1.7) 56(84) bytes of data.
64 bytes from 200.1.1.7: icmp_seq=1 ttl=62 time=111 ms
64 bytes from 200.1.1.7: icmp_seq=2 ttl=62 time=1.05 ms
64 bytes from 200.1.1.7: icmp_seq=3 ttl=62 time=0.820 ms
--- 200.1.1.7 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2042ms
rtt min/avg/max/mdev = 0.820/37.779/111.467/52.105 ms
pc1:~# █
pc1
pc2:~# ping 195.11.14.5
PING 195.11.14.5 (195.11.14.5) 56(84) bytes of data.
64 bytes from 195.11.14.5: icmp_seq=1 ttl=62 time=0.954 ms
64 bytes from 195.11.14.5: icmp_seq=2 ttl=62 time=0.947 ms
64 bytes from 195.11.14.5: icmp_seq=3 ttl=62 time=1.27 ms
--- 195.11.14.5 ping statistics ---
3 packets transmitted, 3 received, 0% packet loss, time 2049ms
rtt min/avg/max/mdev = 0.947/1.057/1.271/0.153 ms
pc2:~# █
pc2
© Computer Networks Research Group Roma Tre

## Slide 19: proposed exercises
the default route can be statically configured by using route add default gw 195.11.14.1 dev eth0
can you give a command to configure a static route that is equivalent to the default route? route add -net __ netmask __ gw __ dev __

## Slide 20: proposed exercises
not all the routing tables contain a default route
the network of this lab is so simple that routers r1 and r2 can be also configured to exclusively use default routes
try such a configuration and test it